## Slide 1: CEA201 ASSEMBLY LANGUAGE
MASSACHUSETTS INSTITUTE OF TECHNOLOGY
BETA Instruction Set Architecture

## Slide 2: Online simulator
BSim Sandbox:
http://computationstructures.org/exercises/sandboxes/bsim.html
--> Click: Open BSim in a new window to open editor and simulation.

## Slide 3
Reference material:
Appendix_β Documentation.pdf
Tutorial :
Giới thiệu phần mềm BSIM: https://youtu.be/FYT38vagylg
Exam 1: https://youtu.be/NVfPtZpZh6M (Bài cơ bản)
Exam 2: https://youtu.be/AepuJT7Fsmc (symbol, label, mảng)
Exam 3: https://youtu.be/IBmPbye9QLQ (vẽ flowchat, đổi giá trị có điều kiện)
Exam 4: https://youtu.be/l3_n73GFV0g (xđ 3 giá trị có phải 3 cạnh tam giác ko)
Exam 5: https://youtu.be/39CRGA5nwHg (tìm min của 3 ô nhớ)
Exam 6: https://youtu.be/FmneWSSbTlI (tìm ước số chung lớn nhất)
Exam 7: https://youtu.be/j5U9ck1bB40 (tính tổng chuỗi số)

## Slide 6: Exam 1: ALUC Instructions
For the Beta instruction sequence shown below, indicate the 32-bit two's complement values of the specified registers after the sequence has been executed by the Beta. The effect of the instructions is cummulative, later instructions use the values stored by earlier instructions.
.include "beta.uasm"
ADDC(R31,0x11,R1)
SUBC(R1,-1,R2)
DIVC(R2,3,R8)
HALT()
Value left in R1?
Value left in R2?
Value left in R8?
Answer:

## Slide 7: Exam 2: ALU Instructions
For the Beta instruction sequence shown beside, indicate the 32-bit two's complement values of the specified registers after the sequence has been executed by the Beta.
.include "beta.uasm"
ADD(r31, r31, r0)
CMPEQ(r0, r31, r1)
ADD(r1, r1, r2)
MUL(r2, r2, r3)
HALT()
Value left in R0?
Value left in R1?
Value left in R2?
Value left in R3?
Answer:

## Slide 8: Practice assembly language exercises
For all exams, you should make use of the Beta documentation and you can use the Bsim (Beta simulator) to verify the exams.
Note: For complicated assignments, use flowchat or pseodocode.

## Slide 9
1. Interchange two contents from a[1] and a[3].
2. Write a program to do the calculation: a[0]=a[1]+a[2]
3. Divide a[0] by a[1], the integer part stored in a[2], the remaining part stored in a[3].
4. a[0] store the value of minutes. Convert the number of minutes to hour and store in a[1] and store the remaining one in a[2]. (For example: a[0] = 125, then a[1] = 2 and a[2] = 5).
5. a[0] store the value of hours. Convert the number of hours to week and store in a[1] and store the remaining days in a[2] and the remaining hours in a[3]. (For example: a[0] = 497 then a[1] = 2, a[2] = 6 and a[3]=17.
6. If a[1] > a[3], then interchange.
7. Find the minimum value of a[0], a[1] and a[2], the result is stored in a[3].
8. Find the maximum value of a[0], a[1] and a[2], the result is stored in a[3].
9. Check if a[0], a[1] and a[2] are the lengths of the triangle. If it is true, store 1 to a[3], otherwise store 0.
10. Sort a[0], a[1] and a[2] in ascending order.

## Slide 10
11. Sort a[0], a[1] and a[2] in descending order.
13. Calculate the sum s = 1 + 2 + ... + a[0] and store it to register r0.
14. Calculate the total number of array elements from a[0] to a[9] and store it to a[10].
15. Find the largest number of array elements from a[0] to a[9] and store it to a[10].
16. Find the largest common divisor of a[0] and a[1] and store it to a[2].
17. Find the smallest common multiple of a[0] and a[1] and store it to a[2].
18. Determine if a[0] is prime number or not. If yes, write 1 to a[1], otherwise write 0.
19. Find the smallest prime number that is greater than a[0], the result is stored in a[1]. (For example, a[0]=8 then a[1]=11).
20. Determine if a[0] is a square number or not. If yes, write 1 to a[1], otherwise write 0.

## Slide 11: Project - Design Problem: Bubble sort
Write 5 programs using the Assemby language to perform the following tasks:
Program 1: Write a program to swap two array elements A[5] and A[6] in Assembly language.
Program 2: Write a program to swap two array elements A[i] and A[i+1] in Assembly language.
Program 3: Write a program to swap two array elements A[i] and A[i+1] if A[i]>A[i+1] in Assembly language. (increasing order)
Program 4: Write a program to sort a data array in increasing order using the "bubble_sort" algorithm.
Program5: Write a program to sort a data array in program 4 using the “selection sort” algorithm.